SPECIFICATION

# ULTRASONIC SENSOR SERIES

The Ultrasonic Sensor has the features of higher

sensitivity and sound pressure level,  small size,  high

reliability,  low  power  consumption,  and  excellent

characteristic against temperature and humidity.

1、Applications:

| Distance measurement | Visitor informer |
| --- | --- |
| Back sensor of automobile | Parking meters |
| Automatic door control | Level measurement |
| Counting devices | Intrude alarm |
| Proximity sensor | Toys |
| Remote control devices | Vehicle detection |

2、Specifications:

| Part Number | 10CK40B(M) 10CK40B(P) | 10CK40R/T(M) 10CK40R/T(P) | 10CK60R/T(M) 10CK60R/T(P) | 12CK40R/T(M) 12CK40R/T(P) | 12CK40B(M) 12CK40B(P) | 16CK40B(M1) 16CK40B(P) |
| --- | --- | --- | --- | --- | --- | --- |
| Construction | Open style |
| Using method | Dual Use | Receiver and Transmitter | Dual Use |
| Nominal frequency | 40 kHz | 60 kHz | 40 kHz |
| Overall sensitivity* | -54dB Min. |  |  |  | -52dB Min. | -50dB Min. |
| Sensitivity (dB)* | -63±3 | -63±3 | -65±3 | -63±3 |  |  |
| S. P. L. (dB)* | 120±3 | 120±3 | 120±3 | 120±3 |  |  |
| Decay Level | Max. 20mVp-p |  |  |  | Max. 20mVp-p | Max. 20mVp-p |
| Directivity (deg.) | 70° | 80° | 65° | 65° | 50° | 50° |
| Capacitance (pF) | 2,000±20% | 2,000±20% | 2,000±20% | 2,500±20% | 2,500±20% | 2,000±20% |
| Using Temp. Range | -30~85℃ | -40~85℃ | -40~85℃ | -40~85℃ | -30~85℃ | -30~85℃ |
| Detectable Range | 0.2~4m | 0.2~4m | 0.2~4m | 0.2~4m | 0.2~4m | 0.2~4m |
| Resolution (mm) | 9 | 9 | 9 | 9 | 9 | 9 |
| Dimensions (mm) | Φ10×7.2 | Φ10×7.2 | Φ10×7.2 | Φ12.6×9.2 | Φ12.6×9.2 | Φ16×12 |
| Max Input Voltage | 20Vp-p Pulse width 0.4ms Interval 100ms | Continuous signal 20Vp-p | Continuous signal 20Vp-p | Continuous signal 20Vp-p | 100Vp-p Pulse width 0.4ms Interval 100ms | 100Vp-p Pulse width 0.4ms Interval 100ms |